## Slide 1: Basics of an Electroluminescence Time Projection Chamber (EL TPC)
EDIT 2012
Fundamentals Group:
James White, Clement Sofka, Andrew Sonnenschien,
Lauren Hsu, Ben Loer, Chris Stoughton, Fritz Dejongh,
Hugh Lippincott, Jong Hee Yoo

## Slide 2: LESSON
Concept of Electroluminescent Time Projection Chamber (EL TPC) – uniform drift field and parallel plate EL gap
Scintillation mechanism in noble gases
Electron drift and diffusion in gases
Electroluminescence: aka light gain / proportional scintillation
Estimate charge yield of alpha in argon gas
Estimate EL yield
Will study the concept using a toy: ”EL TPCito”

## Slide 3: EL TPC Physics Detectors
ZEPLIN II/III two-phase xenon WIMP search
XENON 10/100 two-phase xenon WIMP search
LUX two-phase xenon WIMP search
WARP two-phase argon WIMP search
DarkSide two-phase argon WIMP search
PANDA-X two-phase xenon WIMP search
NEXT-100 high pressure xenon 0νββ search
many other prototypes for reactor monitoring, homeland defense, medical …

## Slide 4: Concept How does it work?
EL Gap
Interaction
and
Drift Region
E-field
Light detectors
Anode
Gate
Cathode
Gamma
(for example)
Deposits energy
Flash of scintillation (S1)
Time
S1
S2
Electroluminescence (S2)
Electron drift

## Slide 5: Example: LUX
50
cm
50
cm

## Slide 6
e.g. High Pressure Xenon TPC
60 keV Gamma
30 keV e-
30 keV e-
30 keV
X-ray
Neutron
(or
WIMP)
S1
S2

## Slide 7
Why use an EL TPC?
NR discrimination
241Am
137Cs
662 keV
Tracking
30 keV
nuclear recoils
electron recoils
Energy
Resolution

## Slide 8: Scintillation Mechanism e.g.Argon ~1 bar
Atom excited by particle interaction:
Ar* + 2Ar  Ar2* + Ar
Ar2*  2Ar + hν
And, recombination can produce light:
Ar+ + e-  Ar*
128 nm
(Similar in other noble gases)

## Slide 9: Argon Scintillation (cont)
Fast component (singlet)
Slow component
(triplet)
Example of alpha-induced scintillation (S1)
in pure argon at P ~ 50 bar with zero drift
field. (Summed pulses from a high pressure
test cell at TAMU.)
Similar, but single event with a trace of
xenon. Interaction with impurity atoms
greatly alters pulse shape.
Penning effect

## Slide 10: Argon-N2 Scintillation

## Slide 11: Electron Drift
With no electric field, liberated electrons will obtain a Boltzmann energy distribution E ~ kT - some will recombine with the positive ions.
With an electric field E present, electrons will drift with velocity v ~ µ E, where
µ is the electron mobility in the gas
(µ is a function of density, gas mixture etc.)
In presence of E, electrons “heat up” and average energy of collision increases.
The mean-free-path between collisions,
λ = 1/(σ n) where σ is the collision cross section and n is the number density of gas atoms.
Cross section for electron collisions in argon
http://garfield.web.cern.ch/garfield/help/garfield_41.html#Ref0347
Ramsauer
minimum
ionization
excitation
elastic

## Slide 12: Electron Drift (cont)
Example:
σ ~ 4 E-16 cm2 and n ~ 3 E19 /cm3
λ = 1/(4E-16 * 3E19) ~ 8E-5 cm ~ 800 nm
But
σ ~ 1 E-17 cm2 and n ~ 3 E19 /cm3
λ = 1/(1E-17 * 3E19) ~ 3E-3 cm ~ 30 µm
note
Atomic spacing is ~ 1/(3E19)1/3 ~ 3E-7 cm ~ 3 nm
Electron energy distribution in
pure argon, Edrift = 326 V/cm
Garfield/Magboltz output
Ar 1 bar
ArN2(0.2%) 1 bar

## Slide 13: Electron Diffusion
Pure Argon 1 bar, 326 V/cm
Argon 99.8% N2 0.2%
4.5 cm
σ = (2Dt)1/2

## Slide 14: Electroluminescence
At some value of E, the energy of drifting
electrons can exceed energy needed to excite atoms
Excitation
Threshold
11.6 ev
Ionization
Threshold
15.7 eV
Argon: 1 bar, 2133 V/cm
Note, these are above excitation threshold but below ionization
threshold.
This allows optimum energy resolution
because there are no fluctuations added
due to ionization process

## Slide 15: Electroluminescence
http://hdl.handle.net/10316/1463
Thesis of C.M.B. Monteiro, U. Coimbra
Yield in argon
Example: say
N ~ 3 E19 atoms/cc
E = 2100 V/cm
Y/N ~ 0.4E-17 ph cm2 /e-/atom
So
Y = N*Y/N ~ 120 ph/e-/cm
E/N = 7E-17 V cm2 atom-1

## Slide 16: EL TPCito
HV Feed-thrus
Cathode
Field rings
Gate grid
Anode grid
TPB-coated window
PMT
4.6 cm
1.5 cm
HD polyethylene vessel

## Slide 17: EL TPCito (cont)
source location

## Slide 18: Electro-statics
Electric Field Lines
Electric Potential
EL gap
Drift region

## Slide 19: Alpha Signal estimate charge yield
Argon: density =1.7E-03 g/cc
E_alpha ~ 4.6 MeV
Projected Range ~ 7.3E-3g/cm2
Distance ~ 7.3E-3/ 1.7E-3
~ 4.2 cm
241Am Source E_alpha ~ 5.4 MeV
but,Am covered with 0.0002 cm Au
stopping power in Au ~ 220 MeV cm2/g
SO energy loss ~ 220 * 19g/cc*.0002 cm
looses about 0.8 MeV
E_Alpha  5.4 -0.8 ~ 4.6 MeV
http://www.nist.gov/pml/data/star/index.cfm
Stopping power: alphas in argon
W ~ 26.5 ev/ion
4.6E6 ev/26.5 ev/ion
~ 170 k ions/alpha
excluding distance from source to
drift region, est~ 150 k ions drifting
Assuming there is no further material
between the source and the drift region:

## Slide 20: Alpha Signal estimate light yield
Light Yield?
N_ions ~ 150k/alpha
Y ~ 120 ph/e-/cm
x 1.5 cm EL gap = 180 ph/e-
Produce ~ N*Y
~ 2.7E7 128 nm γ’s into 4π
Tetraphenyl - Butadiene (TPB)
Est 100% conversion efficiency
But how many will we detect?
D
PMT
PMMA
EL Gap
d
TPB coating
First, need special window and
PMT to detect 128 nm directly
(e.g. MgF2 window and PMT)
So, use VUV to blue WLS (wavelength shifter)
Back-of-envelope estimate:
PMT: D=5 cm  APMT = π D2/4
d ~ 2.5 cm  Asph=4π d2
ΔΩ/Ω ~~ APMT/Asph ~ D2/(16d2) ~ .25
TPB: 100% conversion, 50% go up, 50% down
QE of PMT ~ 0.2 in blue
Efficiency ~ ΔΩ/Ω *QE*.5(TPB effect)
~ .25*.2*.5 = 1/40 ~ 2.5%
So Detect ~ 2.7E7*.025 = 7E5 pe (photoelectrons)

## Slide 21: Example Signal
Drift time
S1
S2

## Slide 22: Construction
88% 0pen ss mesh anode and gate
mesh placed on field rings
field rings on cathode
hd polyethylene housing with
TPB-coated acrylic window

## Slide 23: PLAN
View internals of toy detector
Assemble HV & signal cables, gas lines, and PMT in dark box
add alpha source and close dark box
turn on gas flow – first pure argon
Apply HV to PMT and observe single electron dark current on oscilloscope
bias cathode to -1500
bias gate grid to 0 V
raise anode voltage to ~ 3000 V and observe S1 & S2 signals
Is drift time from S1 to start of S2 what you expect?
vary drift field and EL field – observe changes
vary gas mixture – add ~ 0.2% N2 – observe change in light yield, drift time
and pulse width – discuss
measure area of single electron pulse – this is tricky!
measure area of S2 pulse  measure light yield – still tricky!
Is light yield reasonable considering back of envelope estimate?
Last, will try window without wavelength shifter –what will happen?