## Slide 1
Silicon Sensors for Collider Physics
from Physics Requirements to
Vertex Tracking Detectors
Marco Battaglia
Lawrence Berkeley National Laboratory,
University of California at Santa Cruz
and CERN, Geneva
EDIT 2012, Silicon Track, February 2012

## Slide 2
Vertex Detectors and Extrapolation Resolution

## Slide 3
Distance from point of closest
approach to primary vertex does
not scale with energy
i.p. = bgct cos a
cos a ~ 1/g
a
i.p.
PVtx
SecVtx
 | b | c | g
<l> (mm) | 3.5 | 1.3 | ~ 0.
ct (mm) | 480 | 217 | ~0.
<Nsec> | 5.1 | 2.7 | ~ 0.
B from H decay at 0.5 TeV
mB = 5.2 GeV, ct = 480 mm
EB = 0.7 x Ejet =
0.7 x 500/4 = 100 GeV
~ 70
<l> ~ 3.5 mm
l = bgct

## Slide 4
Higgs Couplings

## Slide 5
Vertexing in
Heavy Ion Collisions
(SGV Fast Simulation)

## Slide 6
Tracking and Vertexing at LHC
ATLAS at LHC at CERN
(2008-)
pp 7-14 TeV
Hybrid Pixels
1.4 m2
80 M Pixels

## Slide 7
Interaction of Charged Particles in Si

## Slide 8
Interaction of Charged Particles in Si

## Slide 9
Interaction of Charged Particles in Si
120 GeV protons
14 mm Si
300 mm Si
280 eV / mm (m.p.)
3.6 eV per e-h pair
 ~80 e- / mm

## Slide 10
Interaction of Charged Particles in Si
Electrons
90Sr source electron spectrum

## Slide 11
Energy Deposit in Si

## Slide 12
Energy Deposit in Si

## Slide 13
CMS Pixels
beam test results with
500 MeV electrons
Vd = -50 V
m.p. charge value = 18000 e-
Vd = -150 V (fully depleted)
m.p. charge value = 25000 e-
Energy Deposit in Si

## Slide 14
Simulating m.i.p. with IR Laser
Abtet al.,
NIM 423 (1999)

## Slide 15
Position Sensitive Detectors

## Slide 16
Microstrip Detectors (1D segmentation)

## Slide 17
Microstrip Detectors
25 mm pitch microstrip with S/N=75 g spoint = 1.3 mm
Straver et al.,
NIM 348 (1994)

## Slide 18
Double-sided Strip Detectors (1+1D segmentation)

## Slide 19
From Strips (1D) to Pixel (2D) Detectors
2x 1D information
generates ambiguities:
n hits g n2 combinations
of which n2-n are ghosts
Example:
Pattern recognition of
2 particle tracks on
double-sided microstrips
Need real 2D info:
from strip to pixel

## Slide 20
2D Sensor + 1D Readout
Main limitation due to interconnect;
How to bring charge from detector
node to readout node ?
Concerns are length of connections
(capacity), technical feasibility
of high channel density;
Early solution: shift charge from detector node to detector chip periphery:
g Charge Coupled Devices (CCDs)
NA32 Fixed Target
Experiment at
CERN SPS
(1984-1986)
200 GeV p beam on Be
2 layers of CCDs
Observation of
Lc baryon decay

## Slide 21
Sensor
Topology
First Hybrid Pixel Detector for HEP
WA97 Fixed Target
Experiment at
CERN SPS
(1995-1996)
Pb beam on Pb target
Hybrid Pixel Telescope

## Slide 22
2D Sensor + 2D Readout: Hybrid Pixels
Advantages include:
sophisticated signal processing on-pixel
(TOT, trigger, sparsification, calibration, autocorrelation);
decouple process for sensor and readout electronics;
Main Limitations are:
large(r) material budget, pixel cell size limited by electronics cell
and interconnect (bump bonding) pitch (~40 mm).
Pioneered in DELPHI at LEP
and extensively used at LHC;
Great progress in bump bonding
pitch and yields;
Spinoff to imaging (MediPix)

## Slide 23
Pitch Size, Occupancy, Resolution
Binary Readout:
Charge Interpolation:
extrapolated
track
Reco Hit
Cluster
LBNL Pixel
Telescope
1.5 GeV e-
V=100 V, d = 300 mm
scharge ~ 7 mm
V~0 V, d = 15 mm
scharge ~ 15 mm

## Slide 24
Pitch and Charge Sampling
Antinori et al.,
NIM 288 (1990)
CERN WA-92 decay detector:
Microstrip detector with
10 mm pitch and individual
strip readout;
Charge centre of gravity
reconstruction;
Space resolution depends also
on detector thickness:
300mm thick detector has more
charge spread for diffusion
(2 strip clusters) and thus better
sampling compared to 150mm
(1 strip clusters);

## Slide 25
Pitch and Charge Sampling
Gorelov et al.,
NIM 481 (2002)
ATLAS Pixel Tracker: Pixel sensors with 30x382mm2 cells
Spatial resolution with digital and analog readout for various
track incidence angles a:

## Slide 26
Pitch and Charge Sampling
spoint vs. pixel pitch
CMOS pixel sensors
active thickness ~15mm, S/N ~ 20
Winter et al.,
ALCPG 2007
MB et al.,
ALCPG 2007
spoint vs. S/N
CMOS pixel sensors
active thick. ~15mm, pitch 40 mm

## Slide 27
Charge Interpolation
Reduce number of readout channels by using floating intermediate
charge collecting nodes (strips or pixels) capacitively coupled to
readout nodes;
Need to keep
Css > CSG
to minimise
charge loss to
backplane (gnd)

## Slide 28
Charge Interpolation with Floating Nodes
MB et al.,
IEEE TNS 48 (2001)
Test Sensor with interleaved pixels,
100 mm pixel, 200 mm readout pitch:
6 mm
point
resolution
Cip ~ 900 fF
Cbp ~ 400 fF

## Slide 29
2D Sensor & 2D Readout: Monolithic Pixels
Embed both detector
sensitive volume and
(part of) readout
Electronics in same
Si wafer;
Advantages:
Thin devices,
no interconnect,
minimal capacitance;
Challenges:
avoid parasitic charge collection;
ensure high fill factor.
SEM Image of
LDRD-1 Pixel Chip
SiO+
Metal
Epi
Si
Bulk
Si

## Slide 30
2D Sensor & 2D Readout: Monolithic Pixels
MB et al.,
NIM A 654 (2011)
CMOS Pixel sensors on high resistivity
substrate approach charge collection
of hybrid pixels with integrated data
processing capabilities in a single thin
Si layer:
Example Silicon-On-Insulator Pixels
1 mm resolution
with 15 mm pixels

## Slide 31
Track Extrapolation and Vertexing resolution
T966 sz vertex resolution = 230 mm
CLIC sz vertex resolution in B decays = 210 mm
MB et al.,
NIM A593 (2008)
FNAL MBTF T966 Data
120 GeV p on Cu target
LBNL Thin CMOS Pixel Telescope
Extrapolate 3 cm upstream from first Si pixel layer:

## Slide 32
Silicon Track Day 2
Microstrip Detectors from D0 and CDF to be tested with small spot IR laser
Microstrip Detector from CMS to be tested with 90Sr
Landau distribution, depletion
Hybrid Pixel Detector from CMS to be tested with 90Sr
DAQ and readout chip, chip calibration, threshold scan,
Landau distribution, scaling of collected charge vs Vd, cluster analysis
CMOS Monolithic Pixel Detector to be tested with 90Sr (and IR laser)
Visualization of analog pixel signal on oscilloscope, driving clocks,
Landau distribution, determination of sensitive thickness, d ray visalization,
cluster reconstruction and analysis

## Slide 33
DELPHI at LEP at CERN
(1989-2001)
e+e- 89-210 GeV
Microstrip and
Hybrid Pixel Tracker
1 M Pixels
Tracking and Vertexing
at Colliders
SLC at SLD at SLAC
(1989-2001)
e+e- 91.2 GeV
VXD3 CCD Vertex
Detector
307 M Pixels

## Slide 34
Tracking and Vertexing at Future Lepton Collider
e+e- Linear Collider or MuC
(20XX)
e+e- 0.25-5.0 TeV (?)
Monolithic Pixels
~1 B Pixels